## Slide 1
General Purpose I2C
Master Driver Design

## Slide 2: I2C Communication Basics
Web記事 : I2Cで復帰不能になる場合の対策
NXP : I2C-bus specification and user manual
RH850/U2A-EVA Group
User’s Manual: Hardware
Renesas microcontroller
RH850 Family
Rev.1.40 Aug. 2023
Section 2 Pin Functions
Section 6 Interrupts
Section 22 I2C Bus Interface (RIIC)
Section 90 Long-Term System Counter (LTSC)

## Slide 3: GpI2C Hardware Assumption
SCL#[ch]
SDA#[ch]
RH850/U2A
I2C Master
I2C Controller
“RIIC”
Channel [ch]
I2C Slave[M]
I2C Slave[N]
VDD or VIO
I2C Slave Power On/Off
Control
I2C Slave Power On/Off I/O Signal
The number of I2C Slave device is equal to or less than 16 for all I2C bus/Channels.

## Slide 4: GpI2C Design Overview
Port/Pin Configuration
LTSC
Interrupt Controller
RIIC
MCAL/Gpt
Free-run Timer
MCAL/Port
MCAL/I2c
MCAL/Intc
Complex Device Driver/
GpI2C Master : gpi2c_ma.*, gpi2c_ma_cfg.c
Complex Device Driver/
GpI2C Master Interface : gpi2c_ma_if.*
System/
EcuM or
AUTOSAR-OS or
SchedM
Dataflow - Write
Dataflow - Read
Application

## Slide 5: GpI2C - System Integration/Interfaces
Component | Prototypes | Provided/ Required | Integrated from/to
gpi2c_ma.c/h | void vd_g_GpI2cMaInit(void) | Provided | To: System/EcuM
gpi2c_ma.c/h | void vd_g_GpI2cMaDeInit(void) | Provided | To: System/EcuM and/or Complex Dev. Driver
gpi2c_ma.c/h | void vd_g_GpI2cMaMainTask(void) | Provided | To: System/AUTOSAR-O:TASK or SchedM
gpi2c_ma.c/h | void vd_g_GpI2cMaIRQTRx(const U1 u1_a_MA_CH) | Provided | To: System/AUTOSAR-OS:ISR
gpi2c_ma.c/h | void vd_g_GpI2cMaIRQDmaRx(const U1 u1_a_MA_CH) | Provided | To: System/AUTOSAR-OS:ISR

## Slide 6: GpI2C - Application Integration/Interfaces
Component | Prototypes | Provided/ Required | Integrated from/to
gpi2c_ma.c/h | U1 u1_g_GpI2cMaReqTRx(const ST_GP_I2C_MA_REQ * st_ap_REQ) | Provided | To: Application
gpi2c_ma.c/h | U2 u2_g_GpI2cMaRwcRembySla(const U1 u1_a_SLA) | Provided | To: Application See
gpi2c_ma.c/ gpi2c_ma_cfg.c/ gpi2c_ma_cfg_private.h | void (*st_gp_GP_I2C_MA_SLA[].fp_vd_ACK)(const ST_GP_I2C_MA_REQ * st_ap_ACK) | Required | From: Application To: gpi2c_ma.c/ vd_g_GpI2cMaMainTask
gpi2c_ma.c/ gpi2c_ma_cfg.c/ gpi2c_ma_cfg_private.h | void vd_g_GpI2cMaCfgInit(void) | Required | To: gpi2c_ma.c/ vd_g_GpI2cMaInit
gpi2c_ma.c/ gpi2c_ma_cfg.c/ gpi2c_ma_cfg_private.h | U1 u1_g_GpI2cMaCfgSlaActvtd(const U1 u1_a_CH) | Required | From: Application or Complex Dev. Driver MCAL To: gpi2c_ma.c/ vd_g_GpI2cMaMainTask

## Slide 7: GpI2C - System Integration/Interfaces
Priority=MidのInterfaceは同割り込み優先度を持つTASK/ISR=Interrupt Service Routineで実行すること。
Priority=High/vd_g_GpI2cMaIRQTRx, vd_g_GpI2cMaIRQDmaRxの実行優先度および遅延時間制約はI2C通信を利用するアプリケーション提供機能に対する性能目標/制約かつソフト全体性能目標に基づいて設計すること。I2C通信に利用される割り込み/ISRの実行遅延が発生してもI2C通信プロトコル・RH850/U2A内臓I2C Controllerの仕組み上,送受信データ上書きよる通信データ不良は発生しない。
Priority=High/vd_g_GpI2cMaIRQTRxはINTRIIC[ch]TI/INTRIIC[ch]RI/INTRIIC[ch]EE/INTRIIC[ch]TEIの全ISRにて実行すること。INTRIIC[ch]TI/RI/EE/TEIは同じ割り込み優先度を設定してINTRIIC[ch]TI/RI/EE/TEIのISRは相互排他となるようSystem/Operating System等をConfigurationすること。
Priority=High/vd_g_GpI2cMaIRQDmaRxはDMA転送完了割り込みにて実行すること。 vd_g_GpI2cMaIRQDmaRxとvd_g_GpI2cMaIRQTRxは相互排他となるよう同じ割り込み優先度を設定すること。
Priority=High/Mid Interface間割り込み排他制御は、Priority=MidのInterface内で行われるのでGpI2C提供InterfaceとI2C Controller以外の割り込みを利用するGpI2C以外のコンポーネントと連動しない場合はGpI2C利用側での排他制御は追加不要。
vd_g_GpI2cMaInit
vd_g_GpI2cMaDeInit vd_g_GpI2cMaMainTask
u1_g_GpI2cMaReqTRx
u2_g_GpI2cMaRwcRembySla vd_g_[Application]MainTask
vd_g_GpI2cMaIRQTRx
vd_g_GpI2cMaIRQDmaRx
TASK/ISR Priority
Priority=High
Priority=Mid
RH850/U2A-EVA Group User’s Manual: Hardware
Renesas microcontroller RH850 Family Rev.1.40 Aug. 2023
Section 22 I2C Bus Interface (RIIC)

## Slide 8: GpI2C - MCAL Interfaces 1/5
Component | Prototypes | Provided/ Required | Integrated from/to
gpi2c_ma_if.c/h | U2 u2_g_GpI2cMaIfFrt(void) | Provided | From: MCAL/Gpt/gpt_drv_frt To: gpi2c_ma.c/ vd_g_GpI2cMaMainTask vd_g_GpI2cMaIRQTRx u1_g_GpI2cMaReqTRx
gpi2c_ma_if.c/h | void vd_g_GpI2cMaIfEnaCh(const ST_GP_I2C_MA_CH * st_ap_CH, const U1 u1_a_PIN_ACT) | Provided | From: MCAL/Dma MCAL/I2c MCAL/Port To: gpi2c_ma.c/ vd_g_GpI2cMaMainTask u1_g_GpI2cMaReqTRx
gpi2c_ma_if.c/h | void vd_g_GpI2cMaIfDisCh(const ST_GP_I2C_MA_CH * st_ap_CH) | Provided | From: MCAL/Dma MCAL/I2c MCAL/Port To: gpi2c_ma.c/ vd_g_GpI2cMaInit vd_g_GpI2cMaDeInit vd_g_GpI2cMaMainTask

## Slide 9: GpI2C - MCAL Interfaces 2/5
Component | Prototypes | Provided/ Required | Integrated from/to
gpi2c_ma_if.c/h | void vd_g_GpI2cMaIfResbyFrT(const ST_GP_I2C_MA_CH * st_ap_CH) | Provided | From: MCAL/Dma MCAL/I2c MCAL/Port To: gpi2c_ma.c/ vd_g_GpI2cMaMainTask
gpi2c_ma_if.c/h | void vd_g_GpI2cMaIfStaTRx(const ST_GP_I2C_MA_CH * st_ap_CH) | Provided | From: MCAL/I2c To: gpi2c_ma.c/ vd_g_GpI2cMaMainTask vd_g_GpI2cMaIRQTRx
gpi2c_ma_if.c/h | void vd_g_GpI2cMaIfWriTx(const ST_GP_I2C_MA_CH * st_ap_CH, const U1 * u1_ap_BYTE_TX) | Provided | From: MCAL/I2c To: gpi2c_ma.c/ vd_g_GpI2cMaIRQTRx
gpi2c_ma_if.c/h | void vd_g_GpI2cMaIfReaRx(const ST_GP_I2C_MA_CH * st_ap_CH, U1 * u1_ap_byte_rx) | Provided | From: MCAL/I2c To: gpi2c_ma.c vd_g_GpI2cMaIRQTRx

## Slide 10: GpI2C - MCAL Interfaces 3/5
Component | Prototypes | Provided/ Required | Integrated from/to
gpi2c_ma_if.c/h | void vd_g_GpI2cMaIfFinTRx(const ST_GP_I2C_MA_CH * st_ap_CH) | Provided | From: MCAL/I2c To: gpi2c_ma.c vd_g_GpI2cMaIRQTRx
gpi2c_ma_if.c/h | void vd_g_GpI2cMaIfResp_Ack(const ST_GP_I2C_MA_CH * st_ap_CH) | Provided | From: MCAL/I2c To: gpi2c_ma.c/ vd_g_GpI2cMaIRQTRx
gpi2c_ma_if.c/h | void vd_g_GpI2cMaIfRespNack(const ST_GP_I2C_MA_CH * st_ap_CH) | Provided | From: MCAL/I2c To: gpi2c_ma.c/ vd_g_GpI2cMaIRQTRx

## Slide 11: GpI2C - MCAL Interfaces 4/5
Component | Prototypes | Provided/ Required | Integrated from/to
gpi2c_ma_if.c/h | void vd_g_GpI2cMaIfIRQ_SeqEI(const ST_GP_I2C_MA_CH * st_ap_CH) | Provided | From: MCAL/I2c To: gpi2c_ma.c/ vd_g_GpI2cMaMainTask vd_g_GpI2cMaIRQTRx u1_g_GpI2cMaReqTRx
gpi2c_ma_if.c/h | void vd_g_GpI2cMaIfIRQ_ReaEI(const ST_GP_I2C_MA_CH * st_ap_CH) | Provided | From: MCAL/I2c To: gpi2c_ma.c vd_g_GpI2cMaIRQTRx
gpi2c_ma_if.c/h | void vd_g_GpI2cMaIfIRQ_WriEI(const ST_GP_I2C_MA_CH * st_ap_CH) | Provided | From: MCAL/I2c To: gpi2c_ma.c vd_g_GpI2cMaIRQTRx
gpi2c_ma_if.c/h | void vd_g_GpI2cMaIfIRQ_DI(const ST_GP_I2C_MA_CH * st_ap_CH) | Provided | From: MCAL/I2c To: gpi2c_ma.c/ vd_g_GpI2cMaIRQTRx
gpi2c_ma_if.c/h | U4 u4_g_GpI2cMaIfIRQst(const ST_GP_I2C_MA_CH * st_ap_CH, const U2 u2_a_SEQ) | Provided | From: MCAL/Dma MCAL/I2c To: gpi2c_ma.c/ vd_g_GpI2cMaIRQTRx

## Slide 12: GpI2C - MCAL Interfaces 5/5
Component | Prototypes | Provided/ Required | Integrated from/to
gpi2c_ma_if.c/h | void vd_g_GpI2cMaIfDmaTxAct(const ST_GP_I2C_MA_CH * st_ap_CH, const U1 * u1p_a_PDU_TX, const U2 u2_a_NBYTE) | Provided | From: MCAL/Dma To: gpi2c_ma.c/ vd_g_GpI2cMaIRQTRx
gpi2c_ma_if.c/h | void vd_g_GpI2cMaIfDmaRxAct(const ST_GP_I2C_MA_CH * st_ap_CH, U1 * u1p_a_pdu_rx, const U2 u2_a_NBYTE) | Provided | From: MCAL/Dma To: gpi2c_ma.c/ vd_g_GpI2cMaIRQTRx
gpi2c_ma_if.c/h | U4 u4_g_GpI2cMaIfDmaRxchk(const ST_GP_I2C_MA_CH * st_ap_CH) | Provided | From: MCAL/Dma MCAL/I2c To: gpi2c_ma.c/ vd_g_GpI2cMaIRQDmaRx
gpi2c_ma_if.c/h | void vd_g_GpI2cMaIfDmaDeAct(const ST_GP_I2C_MA_CH * st_ap_CH) | Provided | From: MCAL/Dma To: gpi2c_ma.c/ vd_g_GpI2cMaMainTask vd_g_GpI2cMaIRQTRx u1_g_GpI2cMaReqTRx

## Slide 13: GpI2C PDU TRx Request/Acknowledgement Sequence
System/
AUTOSAR-OS
Application
GpI2c
RIIC
Interrupt
Controller
vd_g_GpI2cMaInit
vd_g_[App]MainTask
u1_g_GpI2cMaReqTRx
MCAL/I2c
vd_g_GpI2cMaMainTask
vd_g_GpI2cMaIfStaTRx/
vd_g_GpI2cMaIfStaTRx
vd_g_GpI2cMaIfEnaCh/vd_g_I2cStart
vd_g_GpI2cMaMainTask
vd_g_GpI2cMaIRQTRx
st_gp_GP_I2C_MA_SLA[].fp_vd_ACK
Software / Call Stack
Software / Controller Registers Write
Hardware / Interrupt Request
T.B.D. : DMAC use is under consideration
Applicationにてu1_g_GpI2cMaReqTRxをコールされたタイミングでApplicationからのI2C送受信要求の実行完了している場合は、即、I2C送受信を開始する。
vd_g_GpI2cMaMainTask,vd_g_[App]MainTask
の順番で実行することで
Input=I2C PDU受信
I/O変換=Appl
Output=PDU送信
の処理順序を実現。

## Slide 14: GpI2C PDU TRx Request/Acknowledgement 1/2
TRx Request : U1 u1_g_GpI2cMaReqTRx(const ST_GP_I2C_MA_REQ * st_ap_REQ)
TRx Acknowledge : void (*st_gp_GP_I2C_MA_SLA[].fp_vd_ACK)(const ST_GP_I2C_MA_REQ * st_ap_ACK)
/* Control Bit Field */
#define GP_I2C_MA_CBF_BIT_RWC (0x000007ffU) /* Read/Write byte Count : Max.2047 bytes */
#define GP_I2C_MA_CBF_BIT_ERR (0x0001f800U) /* ERRor : */
#define GP_I2C_MA_CBF_BIT_PID (0x0ffe0000U) /* Pdu IDentifier : free to use for application */
#define GP_I2C_MA_CBF_BIT_SLA (0xf0000000U) /* SLAve identifier : see gpi2c_ma_channel.h, GP_I2C_SLA_X */
#define GP_I2C_MA_CBF_LSB_ERR (11U)
#define GP_I2C_MA_CBF_LSB_PID (17U)
#define GP_I2C_MA_CBF_LSB_SLA (28U)
#define GP_I2C_MA_ERR_FR_TOUT (0x00000800U) /* FRame TimeOUT */
#define GP_I2C_MA_ERR_SEQ_UNK (0x00001000U) /* read/write SEQuence UNKnown */
#define GP_I2C_MA_ERR_IRQ_UNK (0x00002000U) /* IRQst UNKnown */
#define GP_I2C_MA_ERR_RWC_UNK (0x00004000U) /* Read/Write byte Counter UNKnown */
#define GP_I2C_MA_ERR_PDU_UNK (0x00008000U) /* st_gp_GP_I2C_MA_CH[].stp_QUE->u1p_PDU == vdp_PTR_NA(NULL) */
#define GP_I2C_MA_ERR_REQ_UNK (0x00010000U) /* Read/Write Request UNKnown */
typedef struct{
U1 * u1p_pdu; /* protocol data unit */
U4 u4_cbf; /* control bit field */
}ST_GP_I2C_MA_REQ;
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
SLA
PID
ERR
RWC
The value shall be set by Application
Free to used for Application
Error bits are set by GpI2C and shall be initialized to zero

## Slide 15: GpI2C PDU TRx Request/Acknowledgement 2/2
Protocol Data Unit
Byte#0
Byte#1
Byte#2
Byte#n-2
Byte#n-1
Read/Write Byte Count = n [bytes]
7
6
5
4
3
2
1
0
Slave/Device Address 7[bits]
R/W
Read = 1b, Write=0b
typedef struct{
U1 * u1p_pdu; /* protocol data unit */
U4 u4_cbf; /* control bit field */
}ST_GP_I2C_MA_REQ;
The memory address of “Byte #0 shall be set by Application
Application
GpI2cMa
FIFO/Queue of ST_GP_I2C_MA_REQ
Pdu R/W Buffer or Const
PDU TRx Request
PDU TRx Acknowledgement
PDU Ack. Timeout
I2C Frame
Timeout
Waning :
PDU TRx Ack. Timeout shall be implemented into Application. It’s because GpI2c can not notify PDU TRx Ack. to application if fatal error is detected such as FIFO/Queue corruption.

## Slide 16: GpI2C Read/Write Byte Count Max/Limitation by Slave 1/2
vd_g_GpI2cMaMainTask
vd_g_GpI2cMaIRQTRx
GpI2C Total Throughput Budge [microseconds]
Execution Cycle of vd_g_GpI2cMaMainTask [milliseconds]
M-PDU#0
M-RWC#0
M-PDU#1
M-RWC#1
M-PDU#m
M-RWC#m
Slave/Device Address 0xYZ/
GP_I2C_SLA_[M], I2C Ch.= [ch]
N-PDU#0
N-RWC#0
N-PDU#1
N-RWC#1
N-PDU#n
N-RWC#n
Slave/Device Address 0xVW
GP_I2C_SLA_[N], I2C Ch.= [ch]
st_gp_GP_I2C_MA_SLA[M].u2_rwc_max
<= M-RWC#0 + M-RWC#1 + .. + M-RWC#m
st_gp_GP_I2C_MA_SLA[N].u2_rwc_max
<= N-RWC#0 + N-0RWC#1 + .. + N-RWC#n
st_gp_GP_I2C_MA_CH[ch].u2_nque >= [number of M-PDU] + [number of N-PDU]＋ 1
送受信 - Read/Write可能なFrame/Byte数の最大/上限値:u2_rwc_maxをSlave毎に設けることで各SlaveI2C-Bus占有時間を確保する。また、I2C通信によるRH850/U2A-CPU占有時間/Throughputも合わせて予測/設計可能とする
PDU送受信要求を一時保存するFIFO/Queueの段数をx段としたい場合は、.u2_nque = x + 1とすること。

## Slide 17: GpI2C Read/Write Byte Count Max/Limitation by Slave 2/2
U2 u2_g_GpI2cMaRwcRembySla(const U1 u1_a_SLA)
Application
[A]
Application
[B]
GpI2C
u2_g_GpI2cMaRwcRembySla(GP_I2C_SLA_[M])
u2_g_GpI2cMaRwcRembySla(GP_I2C_SLA_[N])
u2_t_rwc = ((GpI2C = Activated) and (Req/FIFO = No Control)) ?
st_gp_GP_I2C_MA_SLA[M].u2_rwc_max - u2_gp_gpi2c_ma_rwc_by_sla[M] : 0
u2_t_rwc = ((GpI2C = Activated) and (Req/FIFO = No Control)) ?
st_gp_GP_I2C_MA_SLA[N].u2_rwc_max - u2_gp_gpi2c_ma_rwc_by_sla[N] : 0
u2_gp_gpi2c_ma_rwc_by_sla[]はアプリからのPDU送受信要求に含まれるRead/Write Countを加算、送受信要求の実行完了、Ack通知後に減算した値を保持。
u2_g_GpI2cMaRwcRembySla戻り値 :
GpI2C制御状態に依存した送受信可能なRead/Write byte数。
GpI2C制御状態でApplicationからのPDU送受信要求が受領できない場合は0が戻り値となる。

## Slide 18: GpI2C PDU TRx State Transition 1/12
INA
STA
WRI
WEN
REA
FIN
REQ
Transition at [vd_g_GpI2cMaMainTask or
u1_g_GpI2cMaReqTRx]
Transition at vd_g_GpI2cMaIRQTRx
[ACT]
Transition at [vd_g_GpI2cMaMainTask or
vd_g_GpI2cMaInit or
vd_g_GpI2cMaDeInit]
Seq/State Encode | Full State Name | Description
GP_I2C_SEQ_INA (0xffff) | INActive | I2C PDU送受信禁止/ I2C Controller駆動停止 and I2C端子機能≠SCL/SDA
GP_I2C_SEQ_REQ (6) | wait for pdu trx REQuest | I2C PDU送受信許可/ I2C Controller駆動中 and I2C端子機能=SCL/SDA I2C PDU送受信要求待ち
GP_I2C_SEQ_STA (0) | STArt | I2C Start Condition送信中/検知待ち
GP_I2C_SEQ_WRI (1) | WRIte | I2C Slave書き込みデータ送信中
GP_I2C_SEQ_WEN (2) | Write ENd | I2C Slave書き込みデータ送信中/送信完了待ち
GP_I2C_SEQ_REA (3) | REAd | I2C Slave読み出しデータ受信中/受信完了待ち
GP_I2C_SEQ_RLA (4) | Read LAst | I2C Slave読み出し最終データ受信中/受信完了待ち
GP_I2C_SEQ_FIN (5) | FINish | I2C Stop Condition送信中/検知待ち
RLA
Transition at vd_g_GpI2cMaIRQDmaRx

## Slide 19: GpI2C PDU TRx State Transition 2/12
#define GP_I2C_MA_ERR_FR_TOUT (0x00000800U) /* FRame TimeOUT */
#define GP_I2C_MA_ERR_SEQ_UNK (0x00001000U) /* read/write SEQuence UNKnown */
#define GP_I2C_MA_ERR_IRQ_UNK (0x00002000U) /* IRQst UNKnown */
#define GP_I2C_MA_ERR_RWC_UNK (0x00004000U) /* Read/Write byte Counter UNKnown */
#define GP_I2C_MA_ERR_PDU_UNK (0x00008000U) /* st_gp_GP_I2C_MA_CH[].stp_QUE->u1p_PDU == vdp_PTR_NA(NULL) */
#define GP_I2C_MA_ERR_REQ_UNK (0x00010000U) /* Read/Write Request UNKnown */
#define | Detected at | Description | Seq.Abort/ Ack.u4_cbf:BIT_ERR
GP_I2C_MA_ERR_FR_TOUT | vd_g_GpI2cMaMainTask ->vd_s_GpI2cMaFraTout | See Page.20: I2C Bus Deadlock Detection - Frame Timeout | N/A, but Reset/ Set
GP_I2C_MA_ERR_SEQ_UNK | vd_g_GpI2cMaMainTask ->u4_s_GpI2cMaQueTryPush | st_gp_gpi2c_ma_ctrl[].u2_seq > GP_I2C_SEQ_REQ | N/A, but Reset/ Unset, then Ack. Lost
 | vd_g_GpI2cMaIRQTRx | st_gp_gpi2c_ma_ctrl[].u2_seq > GP_I2C_SEQ_FIN | Abort/ Set
GP_I2C_MA_ERR_IRQ_UNK | vd_g_GpI2cMaIRQTRx ->u4_g_GpI2cMaIfIRQst | I2C Controller Status/st_gp_gpi2c_ma_ctrl[].u2_seq unmatch Refer to gpi2c_ma_stm.xlsx Sheet “u4_g_GpI2cMaIfIRQst” | Abort/ Set
GP_I2C_MA_ERR_RWC_UNK | vd_g_GpI2cMaIRQTRx ->u4_s_GpI2cMaIRQEas_Rwcchk | st_gp_gpi2c_ma_ctrl[].u2_rwc > st_gp_req[].u4_cbf:BIT_RWC | Abort/ Set
GP_I2C_MA_ERR_PDU_UNK | vd_g_GpI2cMaIRQTRx ->u4_s_GpI2cMaIRQEas_Opechk | st_gp_GP_I2C_MA_CH[].stp_QUE[].u1p_PDU == vdp_PTR_NA(NULL) | Abort/ Set
GP_I2C_MA_ERR_REQ_UNK | vd_g_GpI2cMaMainTask ->u4_s_GpI2cMaQueTryPush | PDU TRx Request – FIFO/Queue Push/Pop Parameter: st_gp_gpi2c_ma_ctrl[].u2_req st_gp_gpi2c_ma_ctrl[].u2_run st_gp_gpi2c_ma_ctrl[].u2_ack Any of above are unknown or out of range. | N/A, but Reset/ Unset, then Ack. Lost
 | vd_g_GpI2cMaIRQTRx ->u4_s_GpI2cMaIRQEas_Reqchk | PDU TRx Request – FIFO/Queue Push/Pop Parameter: st_gp_gpi2c_ma_ctrl[].u2_req st_gp_gpi2c_ma_ctrl[].u2_run st_gp_gpi2c_ma_ctrl[].u2_ack Any of above are unknown or out of range. | Abort/ Unset, then Ack. Lost

## Slide 20: GpI2C PDU TRx State Transition 3/12
I2C Write Operation without DMA - PDU TRx Request = 1, Write Tx Count = 4
Start
Stop
Bit 7
Bit 6
Bit 5
Bit 4
Bit 3
Bit 2
Bit 1
Bit 0
Byte#0
Slave Device Address
7 [bits]
W(0)
ACK
Byte#1/Data#0
ACK
Byte#2/Data#1
ACK
Byte#3/Data#2
ACK
vd_g_GpI2cMaIRQTRx
STA
WRI
WEN
FIN
REQ
REQ
●INTRIIC[ch]EE
EI
DI
DI
▼INTRIIC[ch]RI
DI
■INTRIIC[ch]TI
EI
DI
DI
◇INTRIIC[ch]TEI
EI
DI
DI
Enable/Disable Interrupt
●
■
■
■
◇
●
□
DMAC利用を想定してINTRIIC[ch]RIと■INTRIIC[ch]TIを同時に割り込み禁止にしている
Master Tx
Slave Tx
■INTRIIC[ch]TI/Tx Buffer Empty禁止/割り込み発生しない。

## Slide 21: GpI2C PDU TRx State Transition 4/12
I2C Write Operation with DMA - PDU TRx Request = 1, Write Tx Count = 4
Bit 7
Bit 6
Bit 5
Bit 4
Bit 3
Bit 2
Bit 1
Bit 0
●INTRIIC[ch]EE
EI
DI
DI
Enable/Disable Interrupt
■INTRIIC[ch]TI/Tx Buffer Empty禁止/割り込み発生しない。
Master Tx
Slave Tx
■INTRIIC[ch]TI
DI
◇INTRIIC[ch]TEI
EI
DI
DI
▲INTSDMAC[un]CH[ch]
ACT/RUN
INA
INActive
▲INTSDMAC[un]CH[ch]禁止で送信データをDMA転送するので割り込み発生しない。
Transferred by DMA
Start
Stop
Byte#0
Slave Device Address
7 [bits]
W(0)
ACK
Byte#1/Data#0
ACK
Byte#2/Data#1
ACK
Byte#3/Data#2
ACK
STA
WEN
FIN
REQ
REQ
●
□
□
□
◇
●
△
vd_g_GpI2cMaIRQTRx
vd_g_GpI2cMaIRQDmaRx

## Slide 22: GpI2C PDU TRx State Transition 5/12
Byte#2/
Data#1
Start
Stop
Bit 7
Bit 6
Bit 5
Bit 4
Bit 3
Bit 2
Bit 1
Bit 0
Byte#0
Slave Device Address
7 [bits]
W(0)
ACK
Byte#1/Data#0
ACK
vd_g_GpI2cMaIRQTRx
STA
WRI
FIN
REQ
●
■
■
■
●
STA
Start
●
Byte#0
Slave Device Address
7 [bits]
W(0)
ACK
■
Byte#1/Data#0
WRI
PDU Write Request[0]
PDU Write Request[1]
I2C送信割り込みにてエラー検出した場合は送受信Sequence/State Transitionを中断しStop Condition送信要求を発行/実行する。
DMAにて送信データ転送している場合は◇INTRIIC[ch]TEI割り込みでDMA転送エラーを検出、Stop Condition送信要求を発行/実行する
Sequence中断が繰り返し発生する可能性があるため、送受信Sequence中断時はFrame Timeout検出用Free-run Timer Counter Captureを実行しない。
Things To Do for EPSW:
Tx Buffer EmptyにてStop Condition送信を実行するとI2C通信波形がどのように変化するかを実機にて確認しておくこと。
Master Tx
Slave Tx
STA
●
■
WRI
STA
WEN
FIN
REQ
●
□
□
◇
●
vd_g_GpI2cMaIRQTRx
vd_g_GpI2cMaIRQDmaRx
Start
Byte#0
Slave Device Address
7 [bits]
W(0)
ACK
Byte#1/Data#0
Start
Stop
Byte#0
Slave Device Address
7 [bits]
W(0)
ACK
Byte#1/Data#0
ACK
ACK
□
PDU Write Request[0]
PDU Write Request[1]
I2C Write Abort - PDU TRx Request > 1, Write Tx Count = 4

## Slide 23: GpI2C PDU TRx State Transition 6/12
Enable/Disable Interrupt
I2C Read Operation without DMA - PDU TRx Request = 1, Read Rx Count = 4
●INTRIIC[ch]EE
EI
DI
DI
▼INTRIIC[ch]RI
DI
EI
DI
■INTRIIC[ch]TI
DI
◇INTRIIC[ch]TEI
EI
DI
DI
Start
Stop
Bit 7
Bit 6
Bit 5
Bit 4
Bit 3
Bit 2
Bit 1
Bit 0
Byte#0
Slave Device Address
7 [bits]
R(1)
ACK
Byte#1/Data#0
ACK
Byte#2/Data#1
ACK
Byte#3/Data#2
NAK
Master Tx
Slave Tx
vd_g_GpI2cMaIRQTRx
●
▼
▼
▼
▼
●
STA
REA
FIN
REQ
REQ
RLA
□
■INTRIIC[ch]TI/Tx Buffer Empty禁止/割り込み発生しない。

## Slide 24: GpI2C PDU TRx State Transition 7/12
Enable/Disable Interrupt
I2C Read Operation with DMA - PDU TRx Request = 1, Read Rx Count = 4
●INTRIIC[ch]EE
EI
DI
DI
▲INTSDMAC[un]CH[ch]
ACT/RUN
INA
INActive
▼INTRIIC[ch]RI
DI
EI
DI
EI
DI
Transferred by DMA
Start
Stop
Bit 7
Bit 6
Bit 5
Bit 4
Bit 3
Bit 2
Bit 1
Bit 0
Byte#0
Slave Device Address
7 [bits]
R(1)
ACK
Byte#1/Data#0
ACK
Byte#2/Data#1
ACK
Byte#3/Data#2
NAK
Master Tx
Slave Tx
●
▼
▽
▼
▼
●
▲
vd_g_GpI2cMaIRQTRx
vd_g_GpI2cMaIRQDmaRx
STA
REA
FIN
REQ
REQ
RLA

## Slide 25: GpI2C PDU TRx State Transition 8/12
Enable/Disable Interrupt
I2C Read Operation with DMA - PDU TRx Request = 1, Read Rx Count = 4
●INTRIIC[ch]EE
EI
DI
DI
▲INTSDMAC[un]CH[ch]
ACT/RUN
INA
INActive
▼INTRIIC[ch]RI
DI
EI
DI
EI
DI
Transferred by DMA
Start
Stop
Bit 7
Bit 6
Bit 5
Bit 4
Bit 3
Bit 2
Bit 1
Bit 0
Byte#0
Slave Device Address
7 [bits]
R(1)
ACK
Byte#1/Data#0
ACK
Byte#2/Data#1
ACK
Byte#3/Data#2
NAK
Master Tx
Slave Tx
●
▼
▽
▽
▼
●
△
vd_g_GpI2cMaIRQTRx
vd_g_GpI2cMaIRQDmaRx
STA
REA
FIN
REQ
REQ
RLA
▲
DMA転送完了割り込み実行開始が最後のデータ受信完了時より遅延した場合はvd_g_GpI2cMaIRQDmaRx内で送受信制御・状態遷移を実行する
受信データ読み出し実行するまで次データの送受信は開始されないようI2C ControllerをConfigurationする。
I2C受信割り込み禁止のためI2C受信割り込み発生しない。

## Slide 26: GpI2C PDU TRx State Transition 9/12
I2C Read Abort without DMA - PDU TRx Request > 1, Read Rx Count = 4
Stop
Bit 7
Bit 6
Bit 5
Bit 4
Bit 3
Bit 2
Bit 1
Bit 0
Byte#1/Data#0
ACK
Byte#2/Data#1
NAK
Master Tx
Slave Tx
vd_g_GpI2cMaIRQTRx
▼
▼
●
Start
Byte#0
Slave Device Address
7 [bits]
R(1)
ACK
●
▼
STA
REA
REQ
RLA
FIN
Start
Byte#0
Slave Device Address
7 [bits]
R(1)
ACK
●
▼
STA
REA
I2C Read操作実行中の中断操作としてStop Conditionを確実に発生するにはMasterからのNACK応答が必要となるのでREA状態からRLA状態へ遷移する。
MasterからACK応答後、即Stop Condition発生するタイミングでSlaveからのSDA=0b/Low出力開始されているとStop Condition不発となり送受信Lockの原因となりうる。
I2C受信割り込み発生＆エラー検出時の動作
  割り込み発生時間/timestampとなるFree-run Timer Counter Captureスキップする
  受信完了したデータはDummy Readを実行して破棄する
  次回受信時エラー検出されるようRead Rx CounterをMaxに設定する
前回エラー検出した場合、Read Rx CounterをMaxに設定しているためエラーGP_I2C_MA_ERR_RWC_UNKが検出され受信データが破棄される。

## Slide 27: GpI2C PDU TRx State Transition 10/12
I2C Read Abort without DMA - PDU TRx Request > 1, Read Rx Count = 4
Stop
Bit 7
Bit 6
Bit 5
Bit 4
Bit 3
Bit 2
Bit 1
Bit 0
Byte#1/Data#0
ACK
Byte#2/Data#1
NAK
Master Tx
Slave Tx
vd_g_GpI2cMaIRQTRx
▼
▼
●
Start
Byte#0
Slave Device Address
7 [bits]
R(1)
ACK
●
▼
STA
REA
REQ
RLA
FIN
Start
Byte#0
Slave Device Address
7 [bits]
R(1)
ACK
●
▼
STA
REA
“RLA”状態にてエラー検出した場合、受信データを破棄、即Stop Conditionが送信される。

## Slide 28: GpI2C PDU TRx State Transition 11/12
I2C Read Abort with DMA - PDU TRx Request = 1, Read Rx Count = 4
Start
Stop
Bit 7
Bit 6
Bit 5
Bit 4
Bit 3
Bit 2
Bit 1
Bit 0
Byte#0
Slave Device Address
7 [bits]
R(1)
ACK
Byte#1/Data#0
ACK
Byte#2/Data#1
ACK
Byte#3/Data#2
NAK
Master Tx
Slave Tx
●
▼
▽
▼
▼
●
▲
vd_g_GpI2cMaIRQTRx
vd_g_GpI2cMaIRQDmaRx
STA
REA
FIN
REQ
REQ
RLA
Start
Stop
Byte#0
Slave Device Address
7 [bits]
R(1)
ACK
Byte#1/Data#0
ACK
Byte#2/Data#1
ACK
Byte#3/Data#2
NAK
●
▼
▽
▽
▼
●
△
vd_g_GpI2cMaIRQTRx
vd_g_GpI2cMaIRQDmaRx
STA
REA
FIN
REQ
REQ
RLA
▲
DMAデータ転送エラーはこの時点のDMA転送完了割り込みで判定しない。
DMAデータ転送DMA転送完了割り込み直後のI2C受信割り込みでDMA転送エラーを判定する。
DMA転送エラーとしてGP_I2C_MA_ERR_IRQ_UNKを記録・ApplicationへAck->u4_cbfにて通知する。

## Slide 29: GpI2C PDU TRx State Transition 12/12
STA
REA
FIN
REQ
Start
Stop
Byte#0
Slave Device Address
7 [bits]
R(1)
ACK
Byte#1/Data#0
ACK
Byte#2/Data#1
ACK
Byte#3/Data#2
NAK
vd_g_GpI2cMaIRQTRx
●
▼
▼
▼
▼
●
Start
Stop
Bit 7
Bit 6
Bit 5
Bit 4
Bit 3
Bit 2
Bit 1
Bit 0
Byte#0
Slave Device Address
7 [bits]
W(0)
ACK
Byte#1/Data#0
ACK
Byte#2/Data#1
ACK
Byte#3/Data#2
ACK
vd_g_GpI2cMaIRQTRx
STA
WRI
WEN
FIN
REQ
●
■
■
■
◇
●
□
STA
STA
Start
Start
●
●
QueueにPushされているPDU送受信要求をすべてpop/送受信完了するまでLoop実行
QueueにPushされているPDU送受信要求をすべてpop/送受信完了するまでLoop実行
Master Tx
Slave Tx
RLA
I2C Read/Write Operation without DMA - PDU TRx Request > 1, Read Rx/Write Tx Count = 4

## Slide 30: I2C Bus Deadlock Detection - Frame Timeout
Start
Bit 7
Bit 6
Bit 5
Bit 4
Bit 3
Bit 2
Bit 1
Bit 0
Byte#0
Slave Device Address
7 [bits]
W(0)
ACK
Byte#1/Data#0
vd_g_GpI2cMaIRQTRx
STA
WRI
WEN
REQ
●
■
■
STA
REA
REQ
Start
Byte#0
Slave Device Address
7 [bits]
R(1)
ACK
Byte#1/Data#0
vd_g_GpI2cMaIRQTRx
●
▼
▼
st_gp_gpi2c_ma_ctrl[ch].u2_frt=u2_g_GpI2CMaFrt()
I2C通信制御割り込み発生＆エラー未検出の場合、割り込み発生時間/timestampとしてFree-run Timer Counter Capture実行
I2C通信制御・割り込み発生からの経過時間
I2C通信制御・割り込み発生からの経過時間
vd_g_GpI2cMaMainTask実行時に割り込み発生時間/timestampを利用して割り込み発生からの経過時間を算出。
割り込み発生からの経過時間 >= st_gp_GP_I2C_MA_CH[ch].u2_fr_tout
でBus Deadlockを検出。リカバリ処置を実行。
リカバリ処置についてはWeb記事 : I2Cで復帰不能になる場合の対策参照
Master Tx
Slave Tx

## Slide 31: GpI2C PDU TRx Req. and Ack. Lost Detection
System/
AUTOSAR-OS
Application
GpI2c
vd_g_[App]MainTask
u1_g_GpI2cMaReqTRx
vd_g_GpI2cMaMainTask
vd_g_GpI2cMaMainTask
st_gp_GP_I2C_MA_SLA[].fp_vd_ACK
vd_g_[App]MainTask
vd_g_GpI2cMaMainTask
st_gp_GP_I2C_MA_SLA[].fp_vd_ACK
vd_g_[App]MainTask
✘
✘
PDU TRx Ack. Timeout
下記条件が発生するとApplicationへのPDU送受信完了Ackが実行されません。
GpI2C PDU送受信要求FIFO/Queue自体およびその制御変数・破壊検出
  ST_GP_I2C_MA_REQ.u4_cbf:SlaveID >= u1_g_GP_I2C_MA_NUM_SLA
u1_g_GpI2cMaCfgSlaActvtd()の戻り値≠TRUE/Activated
Application側でPDU送信Ack. Timeout機能を搭載してください。
u1_g_GpI2cMaReqTRx実行後にAck.Timeoutを開始、Ack.Lost検出してください。

## Slide 32: Things To Do for 電子PFソ技/製品PF1室 1/2
vd_g_GpI2cMaIRQTRxはINTRIIC[ch]TI/INTRIIC[ch]RI/INTRIIC[ch]EE/INTRIIC[ch]TEIの4つのISRから実行するものの複数割り込み要求/IRQが同時発生した場合でもvd_g_GpI2cMaIRQTRx実行は何れかのIRQ/ISRに対して1回のみ実行される前提、すなわちvd_g_GpI2cMaIRQTRx内でPending中のIRQのクリアを実行しPending中のIRQ/ISRはCPU/OSで受理/実行されないことが期待動作となっている。Aubist/AUTOSAR-OSを利用する場合はISR/Category2 or Category1いずれかで前述設計意図通りのISR実行が可能であることを確認すること。
各通信制御状態 GP_I2C_SEQ_XXX毎のvd_g_GpI2cMaIRQTRx - Throughput計測
gpi2c_ma_stm.xlsx Sheet “u4_g_GpI2cMaIfIRQst”に定義してある各通信制御状態 GP_I2C_SEQ_XXX毎、I2C Controller制御状態の実機動作・整合性確認。特にStart Condition検出時のNACKFの値確認
Page20 : GpI2C PDU TRx State Transition 5/12, データ送信中のStop Condition送信実行時・SCL/SDA波形確認
Frame Timeout検出時のu1_g_GpI2cMaIfSynLost・SCL同期ロスト検出とリカバリ処置・効果確認

## Slide 33: Things To Do for 電子PFソ技/製品PF1室 2/2
DMAの転送TriggerをInterfaceで変更・設定できるようにMCAL/DMAの設計・実装変更を検討すること。
  I2C通信 Read/Write操作でDMAによる送信/受信データの転送Triggerを切り替えする必要あり。
  I2C通信 Read/Write操作それぞれでDMA 2Channelを割り当てする設計/実装とするならGpI2Cの設計/実装を変更する必要あり。
RH850/U2A内臓I2C Controller “RIIC”動作確認。Read Operation終了時操作:#1.Stop Condition送信->#2. 受信データ読み出し
  I2C通信波形計測にてStop Condition発生を確認しておくこと
  Stop Condition送信後の受信データ読み出しにて最後に受信したデータの取得が可能であることを確認すること。

## Slide 35: Materials
Pptx Object
Picts